## Slide 1: TSE6 - OpenCL
Part5
Memory optimizations

## Slide 2: What’s the use of OpenCL?
OpenCL is a library that is applicable on many different architectures, ranging from normal CPU’s to GPU’s to FPGA’s
  One program can run on very different architectures
OpenCL can be used as a language to design FPGA’s
  See https://www.altera.com/en_US/pdfs/literature/wp/wp-01173-opencl.pdf
See also: http://amdahlsoftware.com/ten-reasons-why-we-love-opencl-and-why-you-might-too/

## Slide 3: What’s the use of GPGPU?
Using OpenCL (or CUDA) for GPGPU applications has many benefits:
  Accelerate image processing operations
    filters, edge detection, etc
  Accelerate calculations for self driving vehicles
    Optimal path calculations
    Predicting braking distances
    Localization
  Accelerate calculations for robotics
    For keeping balance while walking
    Controlling the motors
    Feedback loop
  Accelerate all kinds of other mathematical calculations
    Especially those involving matrix/vector calculations
    Fluid dynamics
    Molecular dynamics
    Weather forecasting
  Create special effects in 3D rendering
    By combining OpenCL with OpenGL
  But also:
    Less power consumption than CPU for the same calculations (https://www.youtube.com/watch?v=sDrz-w1jzEU)

## Slide 4: OpenCL Hardware Model
=core

## Slide 5: SW  HW mapping
Each Work Item (=Thread) is executed on a Processing Element (=Compute Element=core)
  Several Work Items can run on one Processing Element
Each Work Group is executed on a Compute Unit
  Several Work Groups can run on one Compute Unit
Kernel is running on a Compute Device

## Slide 6: OpenCL SW Memory Model
In an OpenCL program, we can define several memory types
  Private Memory
    Per work-item
  Local Memory
    Shared within a workgroup
  Global/Constant Memory
    Shared between all workgroups
On the CPU
  Host Memory
See also OpenCL Memory Spaces
Memory management is explicit
You must move data from host  global  local … and back

## Slide 7: Memory organization in general
Memory is usually addressed on byte level
  Every byte has its own address
The bytes are divided into banks
  For example: memory can be divided into 4 banks, each bank 2 bytes wide:
  Restriction: we can not access 2 rows of 1 bank at the same time
    We can access all the green addresses simultaneously
    We can not access the red addresses simultaneously
      The two red rows will be accessed sequentially  takes double time!
      This is a BANK CONFLICT
Bank 0 | Bank 1 | Bank 2 | Bank 3
0,1 | 2,3 | 4,5 | 6,7
8,9 | 10,11 | 12,13 | 14,15
16,17 | 18,19 | 20,21 | 22,23
… | … | … | …
Bank-row

## Slide 8: General rules for optimal memory access
Accessing 1 byte from a bank-row is as fast as accessing all bytes from that row
  General rule: access memory as much as possible per bank-row
Accessing bytes from different rows of the same bank takes 2 accesses
  General rule: avoid accessing 2 rows of the same bank simultaneously

## Slide 9: Global memory on GPU
Global GPU memory is the biggest bottleneck
  Accesses to global memory take a lot of time
    Typically 200 to 800 nsec per access
  Compare this to the clock speed of the cores:
    Suppose1GHz  1 nsec per clock cycle
One global memory operation takes 100s of clock cycles

## Slide 10: Thread switching
What happens during a global memory access?
  This time is not wasted:
    The threads that did the memory request are put on hold
    The cores switch to another set of threads and execute these
    These new threads might also have to wait for read/write
    Then the cores switch to yet another set of threads
    And so on…
Important fact: on a GPU, thread switching takes almost no time
  A core can switch very fast from one thread to another
Important rule: keep occupancy high enough
  There should always be enough threads (workgroups) allocated on a CU, so that the cores can switch to another set of threads when they have to wait for global memory access

## Slide 11: Global memory organization
Global memory is often organized as 1 very wide bank
  Typically 8 bytes or more, like:
In this case, for example:
  bytes 16 – 23 can be read in 1 access
  bytes 12 – 19 have to be read in 2 accesses
  if byte 12 is being read, bytes 8-11 and 13-15 are also cached
Bank 0
0, 1, 2, 3, 4, 5, 6, 7
8, 9,10,11,12,13,14,15
16,17,18,19,20,21,22,23
24,25,26,27,28,29,30,31
…

## Slide 12: Memory coalescing
To coalesce = to join together (Dutch: samenvoegen)
Threads in a work group should access global memory addresses sequentially
  For example, if there are 16 threads executing the same kernel, 16 sequential positions in global memory (1 position per thread) can be accessed in the same time that it would take 1 thread to read 1 position in memory
  If all memory accesses are performed this way, performance can speed up by a factor of 16 (in the memory access code)

## Slide 13: Coalesced
Optimal way to access memory
  All thread accesses are sequentially, and within the same block
  Everything can be read in 1 access

## Slide 14: Non consecutive
Quite unpredictable
  All thread accesses are within the same block, but not sequentially
  Depending on the platform, this could lead to 16 accesses
  Newer devices (CC1.2 and higher) handle this better (1 access)

## Slide 15: Misaligned
Not so optimal way
  All thread accesses are sequential, but in consecutive blocks
  Takes 2 or more accesses

## Slide 16: Strided access
Not so optimal
  Consecutive threads skip one or more memory addresses
  Multiple memory accesses are needed, depending on the stride
Stride=2

## Slide 17: General guidelines
Let consecutive threads access global memory addresses consecutively
Make sure that there are ‘enough’ workgroups available per CU, so that cores can always switch to non-waiting threads

## Slide 18: Local memory organization
Local memory is often organized as several narrow banks
  Typically 4 bytes per bank
  Assume a is an array of int’s, and we have 8 banks:
Bank 0 | Bank 1 | Bank 2 | Bank 3 | Bank 4 | Bank 5 | Bank 6 | Bank 7
a[0] | a[1] | a[2] | a[3] | a[4] | a[5] | a[6] | a[7]
a[8] | a[9] | a[10] | a[11] | a[12] | a[13] | a[14] | a[15]
… | … | … | … | … | … | … | …

## Slide 19: Example: Fermi local memory
Fermi has 32 banks which are 4 bytes wide
See here for more explanation

## Slide 20: Reduction kernel 2 revisited
Values (Local Memory)
0
1
2
3
4
5
6
7
0
1
2
3
0
1
0
Local IDs
Values
Local IDs
Values
Local IDs
Values
Local IDs
Step 1
Stride 1
Step 2
Stride 2
Step 3
Stride 4
Step 4
Stride 8
10 | 1 | 8 | -1 | 0 | -2 | 3 | 5 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
11 | 1 | 7 | -1 | -2 | -2 | 8 | 5 | -5 | -3 | 9 | 7 | 11 | 11 | 2 | 2
18 | 1 | 7 | -1 | 6 | -2 | 8 | 5 | 4 | -3 | 9 | 7 | 13 | 11 | 2 | 2
24 | 1 | 7 | -1 | 6 | -2 | 8 | 5 | 17 | -3 | 9 | 7 | 13 | 11 | 2 | 2
0
2
4
6
8
10
12
14
10 | 1 | 8 | -1 | 0 | -2 | 3 | 5 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
Values (Global Memory)
1
3
5
7
9
11
13
15
Copy from Global to Local
Copy result back to Global
0
41
41 | 1 | 7 | -1 | 6 | -2 | 8 | 5 | 17 | -3 | 9 | 7 | 13 | 11 | 2 | 2

## Slide 21: Example of memory bank conflict
In reduction kernel, version 2 (week 2), 8 threads active in step 1
Suppose again we have 8 banks, each 1 int (4 bytes) wide:
Thread 0 accesses first a[0] and then a[1], and thread 4 accesses first a[8] and then a[9],  bank conflict
Similar for all the other threads
Similar in all other steps
Bank 0 | Bank 1 | Bank 2 | Bank 3 | Bank 4 | Bank 5 | Bank 6 | Bank 7
a[0] | a[1] | a[2] | a[3] | a[4] | a[5] | a[6] | a[7]
a[8] | a[9] | a[10] | a[11] | a[12] | a[13] | a[14] | a[15]
… | … | … | … | … | … | … | …

## Slide 22: How to avoid memory bank conflicts
What goes wrong exactly in the previous kernel?
  Threads perform the addition with the following statement:
    sdata[index] += sdata[index+s]; where index = 2*s*tid:
  This statement is executed as follows:
    Read sdata[index] from memory
    Read sdata[index+s] from memory
    Add the 2 values in the core
    Write the result to sdata[index]
  Note: the cores execute the above 4 steps in lock-step: all do the same at the same time with different values for index
    In all the steps 1), 2) and 4) memory bank conflicts occur
  It would be better if, in step 1), 2) and 4), subsequent cores access subsequent memory locations

## Slide 23: Reduction kernel 4: sequential access
Values (Local Memory)
Local IDs
Values
Local IDs
Values
Local IDs
Values
Local IDs
Step 1
Stride 1
Step 2
Stride 2
Step 3
Stride 4
Step 4
Stride 8
0
2
4
6
8
10
12
14
10 | 1 | 8 | -1 | 0 | -2 | 3 | 5 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
Values (Global Memory)
1
3
5
7
9
11
13
15
Copy from Global to Local
Copy result back to Global
0
41
10 1 8 -1 0 -2 3 5 -2 -3 2 7 0 11 0 2
0
1 2 3 4 5 6 7
0
1 2 3
0
1
0
8 | -2 | 10 | 6 | 0 | 9 | 3 | 7 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
8 | 7 | 13 | 13 | 0 | 9 | 3 | 7 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
21 | 20 | 13 | 13 | 0 | 9 | 3 | 7 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
41 | 20 | 13 | 13 | 0 | 9 | 3 | 7 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2

## Slide 24: Useful links
A similar discussion about optimization, but applied to dot-product: http://www.cmsoft.com.br/opencl-tutorial/optimization-strategies/
A short article about memory coalescing: http://www.azavea.com/blogs/labs/2010/07/gpu-memory-bandwidth/
About dynamical Local Memory allocation: http://www.openclblog.com/2014/10/allocating-local-memory.html