## Slide 1: TSE6 - OpenCL
Part 1
Introduction

## Slide 2: Class introduction
Week planning (subject to change)
All assignments, except the first, must be marked sufficiently
In the final project, you solve a problem of your own choice
  “It’s working” is not enough; some degree of optimization is required
Week | Theory | Practical
1 | Weird week | 
2 | Introduction OpenCL | Assignment 1 (not graded)
3 | Memory types OpenCL | Assignment 2
4 | Synchronization | Assignment 3
5 | OpenCL and OpenGL | Assignment 4
6 | Memory Optimization | Assignment 5; proposal for final project
7 | Easter Monday | 
8 |  | Work on final project
9 | Final project must be handed in on Wednesday; will be graded within a week | 
10 | If not sufficient, repairs can be done in this week | 

## Slide 3: Evolution of processors

## Slide 4: Why GPU’s?
Graphical Processing Unit
Primarily designed to do calculations in the field of 3D CGI, like:
  Transformations
  Filtering
  Texture operations
Typically matrix operations, and locally concentrated operations  SIMD
GPU highly optimized for these operations, much faster than CPU
GPU can do other types of calculations  GPGPU (General Purpose GPU)
Usually programmed in C(++)-like way, using:
  OpenCL (ATI and nvidia)
  CUDA (nvidia)

## Slide 5: Why GPU’s?
More % of silicon dedicated to computations (green)
Less is needed for control&cache (yellow/orange)

## Slide 6: GPU/CPU performance comparison

## Slide 7: Introduction into OpenCL
OpenCL is a programming framework for heterogeneous computing resources
Suitable for CPUs, GPUs, Cell Broadband Engine, FPGAs, DSPs
It’s a standard, with several implementations from all major companies (AMD, Intel, nvidia, …)
Many introductions available; just two of them:
  A gentle intoduction to OpenCL
  OpenCL programming book
Competing framework is CUDA
  Specifically for nvidia GPU’s
  Made and maintained only by nvidia
  Less general, but can be more efficient

## Slide 8: Design goals of OpenCL
Use all computational resources in system
  GPU’s and CPU’s as peers
  Data- and task-parallel compute model
Efficient parallel programming model
  Based on C
  Abstracts the specifics of underlying hardware
Specify accuracy of floating point computations
  IEEE754 compliant rounding behavior
  Define maximum allowable error of math functions
Drive future hardware requirements

## Slide 9: OpenCL versions
Initially developed by Apple, now maintained by Khronos group
First approved for public release in Nov 2008
Currently at version 2.1 (Nov 2015)

## Slide 10: OpenCL Hardware Model
OpenCL can run on diverse range of hardware, but the general model is always the same
There is one Host, and any number of Compute Devices (CD)
  A Compute Device is usually your graphics card, but can be any CPU, GPU, FPGA, etc
  Each Compute Device is composed of one or more Compute Units (CU)
    Each Compute Unit is further divided into one or more Processing Elements (PE)
      Each PE is like a small processor (core)
      Each PE can do FP instructions, etc
      All PE’s in one CU execute the same instructions in SIMD/SPMD fashion

## Slide 11: OpenCL Hardware Model

## Slide 12: Example Compute Device: nvidia Fermi GPU
This is one CD
Contains 16 CU’s (=SM=Streaming Multiprocessor)
32 PE’s (=cores) per CU
   512 cores total
Latest nvidia GPU (Maxwell) has 2048 cores

## Slide 13: OpenCL Software Execution Model
An OpenCL application runs on the host and submits work to the compute devices
  Kernel: The code which is executed on a PE; basically a C function
  Work item: One instance of the kernel, running on a PE
  Work group: Group of work items running on one CU
  Program: Collection of kernels and other functions
  Context: The environment within which work-items executes
    includes devices and their memories and command queues
  Device Queue: kernel calls are queued in-order
    one queue per device
    executed in-order or out-of-order
Queue
Queue
Context
GPU device
CPU

## Slide 14: SW  HW mapping
Each Work Item is executed on a Processing Element (Compute Element)
Each Work Group is executed on a Compute Unit
  Several Work Groups can run on one Compute Unit
Kernel is running on a Compute Device

## Slide 15: Work Groups
Work Groups can execute in any order, concurrently or sequentially
Fast shared memory and synchronization
Scales across any number of Compute Units

## Slide 16: Writing a kernel
Kernels are written in OpenCL C, a special language, based on C99 with some extensions and limitations
  Extra datatypes
  Extra keywords
  No recursion
  and some more differences, see OpenCL C 2.0 specification
The kernel is an OpenCL C function that
  has to start with __kernel
  can have arguments
  can call other functions from the kernel

## Slide 17: Kernel structure
Example: matrix addition:
Each PE does one single addition
  9 PE’s run in parallel
All PE’s execute exactly the same code (kernel)
How does a PE know which addition it has to do (what are the indices i and j)?
__kernel void addArray
(__global float* A,
__global float* B,
__global float* C
)
{
int w = ..., h = ...; int i = ..., j = ...;
C[i*w+j] = A[i*w+j] + B[i*w+j];
}
We don’t have 2D arrays in OpenCL, so we mimic it with a 1D array

## Slide 18: Kernel dimensions
When starting a kernel, we specify
  how often it must be repeated (how many work items from this kernel)
    global work size
  how many of them have to run on the same CU (how many work items in a work group)
    workgroup size (aka ‘local work size’)
A kernel can be started in 1D (sequence), 2D (matrix) or 3D (cube)

## Slide 19: Kernel dimensions
1-dimensional sequence of work items
  Example: 24 work items, divided in groups of 8
  (global id) = (workgroup id)*(workgroup size)+(local id)
Each work item can query its own position
  global id  get_global_id(0)
  workgroup id  get_group_id(0)
  local id  get_local_id(0)
  workgroup size  get_group_size(0)
  and a few more like these, see Work Item Built-In Functions

## Slide 20: Kernel dimensions
Another 1-dimensional example

## Slide 21: Kernel dimensions
2-dimensional matrix of work items
Sx = get_local_size(0)
Sy = get_local_size(1)
Gx = get_global_size(0)
Gy = get_global_size(1)
wx = get_group_id(0)
wy = get_group_id(1)
sx = get_local_id(0)
sy = get_local_id(1)

## Slide 22: Kernel dimensions
3-dimensional cube of work items
  Similar to 1D and 2D

## Slide 23: How to start a kernel
We can start a kernel with clEnqueueNDRangeKernel(...)
  Specify the dimension/sizes, and the queue in which to place the kernel
  See specs
  Example
    clEnqueueNDRangeKernel (queue, // queue in which to place this kernel kernel, // the kernel itself 1, // number of dimensions (1, 2 or 3) NULL, // ignore for now globalSize, // array with global sizes in each dim localSize, // array with workgroup sizes in each dim 0, // ignore for now NULL, // ignore for now NULL // ignore for now );

## Slide 24: Back to the matrix addition example
It’s a 3x3 matrix, so if we choose workgroupsize 1x1, then we would have to start that with:
  size_t globalsize[]={3,3}, localsize[]={1,1}; clEnqueueNDRangeKernel (queue, kernel, 2, // it’s a 2-dimensional matrix NULL, globalSize, // 3x3 work items globally localSize, // 1x1 work item per group 0, NULL, NULL );
  localSize might be NULL, then OpenCL will choose

## Slide 25: How to configure the kernel
We have to make a number of choices for the kernel:
  How many dimensions
    1D, 2D or 3D
  Global size per dimension
    Example: if we have 16 work items, then 1x16, 2x8, or 4x4
  Size of the workgroups
    Example: if global dimensions are 4x4, workgroup size could be 1x1, 2x2, 4x4, 1x4, 2x4, etc but also 3x3 would be possible
First 2 settings usually follow logically from the problem itself
  Example: if we have to do an operation on a 1000x10 matrix, then we define the kernel to be 2D with a global size of 1000x10
Workgroup size is more critical

## Slide 26: Considerations for workgroup size
One consideration depends on the GPU architecture
  All work items in a work group run on the same CU
    Work group too big (eg same as global dimensions)
       then there is only 1 work group, so only 1 CU will be used
    Work group should not be smaller than size of the CU,
       otherwise some PE’s will be idle
  GPU properties can be queried with clGetDeviceInfo
Some other considerations depend on the chosen algorithm:
  Only work items in the same work group can share (very fast) local memory (see week 2)
  Only work items in the same work group can be synchronized (see week 3)

## Slide 27: Complete OpenCL program
Most basic concepts are described above
Unfortunately, a lot of extra code is needed to
  allocate memory on the Compute Device
  setup a context, kernel, kernel arguments, device queue, etc
  compile the kernel to machine code
  copy information from host memory to device memory and back

## Slide 28
/* Declare (and initialize) all the necessary variables */
......
/* Create OpenCL Context */
context = clCreateContext(NULL, 1, &device_id, NULL, NULL, &ret);
/* Create command queue */
command_queue = clCreateCommandQueue(context, device_id, 0, &ret);
/* Allocate memory for arrays on the Compute Device */
AonDevice = clCreateBuffer(context, CL_MEM_READ_WRITE, 3*3*sizeof(int), NULL, &ret);
BonDevice = clCreateBuffer(context, CL_MEM_READ_WRITE, 3*3*sizeof(int), NULL, &ret);
ConDevice = clCreateBuffer(context, CL_MEM_READ_WRITE, 3*3*sizeof(int), NULL, &ret);
/* Copy arrays A and B from host memory to Compute Devive */
ret = clEnqueueWriteBuffer(command_queue, AonDevice, CL_TRUE, 0, 3*3*sizeof(int), A, 0, NULL, NULL);
ret = clEnqueueWriteBuffer(command_queue, BonDevice, CL_TRUE, 0, 3*3*sizeof(int), B, 0, NULL, NULL);
/* Create kernel program */
program = clCreateProgramWithSource(context, 1, (const char **)&source_str, (const size_t *)&source_size, &ret);
/* Compile the program Just In Time to GPU machine code */
ret = clBuildProgram(program, 1, &device_id, NULL, NULL, NULL);
/* Create OpenCL kernel from the compiled program */
kernel = clCreateKernel(program, “addArray", &ret);
/* Set OpenCL kernel arguments */
ret = clSetKernelArg(kernel, 0, sizeof(cl_mem), (void *)&AonDevice);
ret = clSetKernelArg(kernel, 1, sizeof(cl_mem), (void *)&BonDevice);
ret = clSetKernelArg(kernel, 2, sizeof(cl_mem), (void *)&ConDevice);
/* Activate OpenCL kernel on the Compute Device; see previous slide */
......
/* Transfer result array C back to host */
ret = clEnqueueReadBuffer(command_queue, ConDevice, CL_TRUE, 0, 3*3*sizeof(int), C, 0, NULL, NULL);
This string contains the source code of the kernel program (see previous slide)
This source code string can be hard-coded, or read from a file
The size of a matrix in bytes

## Slide 29: Kernel compilation
Every OpenCL implementation provides a compiler from OpenCL C to supported device executable code
The compiler supports standard set of OpenCL defined options
The kernels can be compiled either online (JIT, run‐time) or offline (build‐time)
  For online compilation, OpenCL C source text is provided to host program  clBuildProgram
  With offline compilation, executable device code is provided to host program
    Run time compilation is more flexible for the final application, but may be problematic in some cases
      Compilation errors need to be extracted from clBuildProgram
      The kernel source code must be included in the application binaries