## Slide 1: TSE6 - OpenCL
Part 2
Memory Model

## Slide 2: Does GPGPU matter?
Facebook uses it for AI (Big Sur):
  http://www.pcworld.com/article/3014321/hardware/facebook-makes-its-big-sur-ai-server-design-available-to-anyone.html
  http://visionandrobotics.nl/2016/02/26/mark-zuckerberg-doneert-25-gpu-servers-voor-onderzoek-naar-machine-learning/
Google is making its own OpenCL/CUDA competitor (GPUCC)
  https://www.phoronix.com/scan.php?page=news_item&px=GPUCC-CUDA-GPGPU-Comp
Google uses it for Machine Learning (deep learning; TensorFlow)
  http://www.wired.com/2015/11/googles-open-source-ai-tensorflow-signals-fast-changing-hardware-world/
Amazon offers GPU computing on their EC2 platforms
  http://docs.aws.amazon.com/AWSEC2/latest/UserGuide/using_cluster_computing.html
Microsoft will offer it soon in Azure
  https://azure.microsoft.com/nl-nl/documentation/videos/azurecon-2015-applications-that-scale-using-gpu-compute/
GPU’s are used for self driving cars and drones
  http://www.neurala.com/gpu-brains-drones-cars/
  http://hackaday.com/2015/11/11/drones-are-getting-a-lot-smarter/
GPU’s and robotics
  http://thepositive.com/robots-in-the-sky/
GPU’s in finance:
  https://www.quora.com/What-are-potential-use-cases-for-GPUs-in-finance

## Slide 3: OpenCL Hardware Model
=core
=GPU + memory

## Slide 4: SW  HW mapping
Each Work Item (=Thread) is executed on a Processing Element (Compute Element)
  Several Work Items can run on one Processing Element
Each Work Group is executed on a Compute Unit
  Several Work Groups can run on one Compute Unit
Kernel is running on a Compute Device

## Slide 5: Host and Device memory
On an average PC, there are 2 big distinct memory areas:
  Host memory
    The normal memory, that is used for any non-GPU program
    Contains variables, stack, heap, etc
    GPU can not use this; only CPU can
  Device memory
    Memory on the graphics card (“video memory”)
    CPU can not use this; only GPU can
Both are connected, usually through a PCI-e bus
  Relatively slow (like 8GBps)
Note: integrated (Intel) GPU shares memory with CPU

## Slide 6: Example system

## Slide 7: Host GPU transfer can be bottleneck
Assume PCI transfer rate of 8 GB/s
Suppose we want to add two 1024x1024 matrices of ints
  Size in bytes per matrix is 1024*1024*4 = 4 MB
  Transfer 2 of these matrices to GPU:
    Theoretical:
      Two times 4 MB, at 8 GBps  1 msec
    Measured around 1.5 msec
  Add the two matrices:
    Theoretical:
      1M additions with 1024 cores, at around 1 GHz  0.001 msec
      Moving all data from/to GPU DRAM, at 177 GBps  0.070 msec
    Measured around 0.800 msec
  Transfer 1 matrix back to host:
    4 MB, at 8 GBps  0.5 msec

## Slide 8: Transfer functions
There are special functions to copy data between host and GPU
  Host  GPU
    clEnqueueWriteBuffer
      Puts a request to copy data from host to device in the queue
      Will be executed when all previous commands are finished
  GPU  Host
    clEnqueueReadBuffer
      Puts a request to copy data from device to host in the queue
      Will be executed when all previous commands are finished
clEnqueueCopyBuffer will copy GPU  GPU

## Slide 9: Mapping functions
With integrated GPU (usually Intel), GPU and CPU share the same memory  copying can be avoided (zero-copy buffer)
Then use the functions clEnqueueMapBuffer/ clEnqueueUnmapMemObject :
  Some example code here:
    http://stackoverflow.com/questions/19972445/whats-the-correct-and-most-efficient-way-to-use-mappedzero-copy-memory-mechan

## Slide 10: Design rule: Minimize transfers between host and GPU
Typical processing flow:
  (1) Transfer data to GPU memory
  (2) CPU sends instructions to GPU
  (3) GPU processes data
  (4) Transfer result to main memory
DeviceHost and HostDevice involve (slow) DMA through PCIe, therefore:
  Only transfer data if necessary
  Combine operations on either CPU or GPU as much as possible
  Might be more advantageous to run ‘slow’ operations also on GPU
  Sequential execution on CPU might be faster than switching between GPU and CPU
Not always predictable, just try

## Slide 11: OpenCL SW Memory Model
In an OpenCL program, we can define several memory types
  Private Memory
    Per work-item
  Local Memory
    Shared within a workgroup
  Global/Constant Memory
    Shared between all workgroups
On the CPU
  Host Memory
See also OpenCL Memory Spaces
Memory management is explicit
You must move data from host  global  local … and back

## Slide 12: Mapping memory types on HW model
Private memory
  Keyword __private or private
  By default, local variables and arguments of a kernel are private
  Allocated locally on the PE as much as possible
    Very fast
    Limited size!
      When PE memory is full, remaining private variables are stored in global memory (slow!)
Local memory
  Keyword __local or local
  Allocated on the CU (Compute Unit)
    Quite fast
    Limited size

## Slide 13: Mapping memory types on HW model
Global memory
  Keyword __global or global
    Allocated on device, outside of GPU chip, in video-memory
      High latency (400 – 800 cycles)
      Throughput around 177 GBps
      Accelerated by using caches
      Big
Constant memory
  Keyword __constant or constant
    Also allocated on device, outside of GPU chip, in video-memory
      Read-only
      Big
More about these qualifiers: link

## Slide 14: Example: nvidia Fermi memory
L2 cache on chip
  768 kB
  Non programmable
  Shared between all SM’s
  128 Byte cachelines
6 Memory Controllers for global memory
  64 bits wide each, so 384 bit in total

## Slide 15: Example: nvidia Fermi memory
Per SM, there is 64 kB that can be used as Local Memory (=Shared Memory) and/or L1 cache
What about Private Memory:
  A PE (=core) does not have its own memory
  PE’s can use parts of the Register File as Private Memory (on average 4 kB per PE)
  When Register File is full, rest of Private Memory is positioned in Global Memory

## Slide 16: Path to memory
On Fermi, memory is divided in 6 partitions, that each have a 64-bit path
  384 bit wide data path
  6 accesses to different memory banks can be done in parallel
  Accesses to the same memory bank have to be serialized
Consequences:
  Let threads in a block access different memory banks
Caching

## Slide 17: Measuring kernel execution time on CPU
Measure this on CPU in Windows with (e.g.) PerformanceCounter
  LARGE_INTEGER freq, start; QueryPerformanceFrequency(&freq); QueryPerformanceCounter(&start); clEnqueueNDRangeKernel(......, &timing_event); clFinish(queue); LARGE_INTEGER end; QueryPerformanceCounter(&end); printf("Kernel execution took %lu milliseconds\n", (double)(end.QuadPart-start.QuadPart)/freq.QuadPart*1000.0);
  Similar for buffer write, read, etc
Wait until the kernel is finished
Get time before kernel starts
Get time after kernel ends

## Slide 18: Measuring kernel execution time on GPU
We can measure this on GPU by using events
  cl_event timing_event; cl_ulong starttime, endtime; clEnqueueNDRangeKernel(......, &timing_event); clFinish(queue); clGetEventProfilingInfo(timing_event,CL_PROFILING_COMMAND_START, sizeof(cl_ulong),&starttime,NULL); clGetEventProfilingInfo(timing_event,CL_PROFILING_COMMAND_END, sizeof(cl_ulong),&endtime, NULL); printf("Kernel execution took %lu nanoseconds\n", endtime - starttime);
  Similar for buffer write, read, etc
We must first enable profiling for this queue:
  queue = clCreateCommandQueue(context, device, CL_QUEUE_PROFILING_ENABLE, &err);
Last argument of clEnqueue...
This event represents the kernel-run
Wait until the kernel is finished
When did the kernel start?
When did the kernel finish?

## Slide 19: Useful links
Introduction in OpenCL: http://www.informit.com/articles/article.aspx?p=1732873
A bit old, but maybe still useful: https://anteru.net/2012/11/03/2009/
An introduction from AMD: http://developer.amd.com/tools-and-sdks/opencl-zone/opencl-resources/introductory-tutorial-to-opencl/